ODIN

OMNEO DIGITAL INTERCOM

REVOLUTIONIZE YOUR INTERCOM ... IN ONE RACK UNIT

- Next-generation intercom matrix provides an unprecedented combination of flexibility, scalability and full-IP performance – all in a compact single rack unit package

- Easy system expansion as your business needs require – up to eight units can be interconnected for a total of 1024 ports

- Offers the broadest interoperability with future, current and legacy RTS products – supports Dante-compatible OMNEO IP technology; allows seamless connectivity between analog two-wire, four wire and digital devices

A new core product in the RTS portfolio, ODIN condenses decades of experience and the latest RTS innovations into a compact single rack unit package that offers state-of-the-art IP technology along with analog connectivity.

Where previous-generation digital matrix products were significantly larger and more costly to own and operate, ODIN’s feature set and form factor are designed to make a professional matrix solution more accessible and easier to use than ever before, opening up the benefits of IP-based communications for wide range of new markets and users of all levels.

In keeping with the RTS principles of forward thinking and backward compatibility, ODIN can seamlessly integrate into the most sophisticated, large-scale intercom operations, extending the value of the initial investment, while also providing a path for system expansion for smaller users who want to upgrade existing RTS systems to the latest technologies.

With connectors for OMNEO IP technology, analog two-wire and four-wire, ODIN supports IP-based ROAMEO wireless systems and KP-Series keypanels, and, as always, analog RTS legacy keypanels. Dante-enabled OMNEO is standard on RJ-45 connectors or is available using optional optical fiber SFP connectors. Users can flexibly define ports to use any of the available connector types. As a user’s capacity needs evolve, a single ODIN can grow from the basic 16 ports to a maximum of 128 ports; up to eight ODIN units can be connected via an optical Inter-Frame Link to create a single matrix with up to 1024 ports. Additional features include redundant power supplies and five cooling fans (two of which are redundant). The unit’s energy-efficient design uses less than 50 watts of power, minimizing operating costs.

The front panel has a color graphical user interface based on icons to support the most common setup and configuration tasks. The AZedit and IPedit software applications have been updated to support ODIN for more complex configuration tasks.

Whether the user wants to increase intercom functionality with an IP-capable system at a regional theater or large house of worship, or whether the goal is to start streamlining a larger system’s footprint and cost of operation in an OB van or broadcast control room, ODIN stands apart as the most comprehensive intercom solution RTS has ever made … all in 1RU.

Key features:

- Compact 1RU form factor makes ODIN perfect for OB vans and other applications where space is at a premium

- Built-in Dante-enabled, AES67 / AES70-compatible OMNEO technology makes the transition to IP easy

- Single unit scalable from 16 to 128 ports

- Port expansion via software upgrade – no additional hardware required

- Up to eight units can be optically interconnected for a total of 1024 ports

- Color display with intuitive icon-based graphical user interface

- Five cooling fans (two of which are redundant)

- Two XLR-connectors for wired partyline in one of three user-selectable formats

- Energy-efficient design – each unit uses less than 50 watts of power for lower cost of ownership

Copy for exploded view image:

ODIN combines the functionality of multiple RTS technologies into one future-proof package:

- The capacity of two OMI-64 cards (64-ports each) — up to 128 channels of digital audio over IP in OMNEO format — fully compatible with Dante and AES67

- Connections for up to 16 analog keypanels

- Inter-Frame-Link connectivity for linking multiple frames together

- A powerful master controller

- Built-in connectors for analog two-wire partyline

- Redundant power supply for an extra layer of protection against failure

Talking points / ad copy (long form):

SCALABLE

Easily expand system as needed by adding licenses or more ODIN units: start with 16 ports, extend up to 128 ports, or connect eight units seamlessly for a 1024-port matrix. No competing product has this level of scalability.

VERSATILE

Offers the broadest interoperability – supports Dante-compatible OMNEO IP technology; allows seamless connectivity between analog two-wire, four wire and digital devices.

USER-FRIENDLY

High-resolution icon-based front-panel color user interface for intuitive operation and immediate configuration directly from the unit.

EFFICIENT

Requires less power, less space and less cooling for lower environmental impact and lower cost of ownership.

FLEXIBLE

Reallocate ports to any hardware type with no adapters or special boards required – future-proof for evolving a system with audio over IP technology; backward compatible with legacy products.

Additional copy from brochure:

A new benchmark for interaction:

With ODIN, all setup and configuration can be done externally by connecting a laptop; the most common operations can be handled directly on the front panel via the icon-driven advanced graphical user interface.

This intuitive GUI makes it easy to get an overview of channel status, or use the menus to quickly find the matrix setting you need to modify. Icons support the most common setup and configuration tasks and are displayed in vivid colors on a high-resolution TFT screen.

The AZedit and IPedit software applications have been updated to support ODIN for more complex configuration tasks.

Get connected:

Whether you use two-wire, wireless, or matrix-based intercoms, ODIN can serve as the core of your RTS system

Use ODIN as the base station for your ROAMEO wireless keypanel beltpack system

ODIN is fully compatible with RTS Trunking technology, allowing ODIN to interoperate with other RTS matrix products including the popular ADAM and ADAM-M

Dante-enabled OMNEO is standard on RJ-45 connectors or is available using optional optical fiber SFP connectors. Users can flexibly define ports to use any of the available connector types.

OMNEO onboard:

The latest generation of RTS advanced digital audio matrix and keypanel products is based upon the uniquely powerful and flexible OMNEO IP technology for media transmission and system control. OMNEO is an architectural approach to connecting devices that need to exchange information such as audio content or device control.

Built upon multiple technologies, including IP and open public standards, OMNEO supports the technologies of today--such as Audinate’s Dante--while adopting the standards of tomorrow. RTS uses OMNEO as our platform to embrace and employ open standards. OMNEO offers a professional-grade media networking solution that provides interoperability, unique features for easier installation, better performance, and greater scalability than any other IP offering on the market.

About RTS:

Innovating the future of global communications:

RTS is the industry leader in professional intercom systems, providing solutions that combine forward-thinking functionality, real-world reliability and superior sound quality.

At the forefront of broadcast intercom technology for over forty years, we are the brand most-trusted by the biggest names in the business. Our family of digital matrices is the most complete and widely used line of intercoms in the world, proven in the most critical and demanding applications.

Today, our latest generation of advanced digital audio matrix and keypanel products is based upon the uniquely powerful and flexible OMNEO IP technology for media transmission and system control. OMNEO has been quickly adopted as the new performance standard by major network customers across the globe for coordinating broadcasts of the world’s largest events via systems of unparalleled size and sophistication.

RTS systems are also scalable for a wide range of applications beyond broadcasting, including in-house production communications for houses of worship and live entertainment, and for failsafe communications in the nuclear power industry. A top priority for us is the backward compatibility of our new products, so they can integrate seamlessly with legacy systems to extend the value of the initial investment. RTS offers the widest variety of matrix interfaces in the market: RVON (VoIP), MADI and OMNEO (Dante plus OCA, AES70), connecting via Ethernet CAT-5e/6, fiber and copper analog.

RTS helps professionals communicate clearly with ease and efficiency, so they can focus on content instead of hardware. Whether for applications large or small, we demonstrate our commitment to our users by innovating the future of global communications.

www.rtsintercoms.com